## Slide 1
BLUETOOTH LOW ENERGY (BLE) FUNDAMENTALS and ESP32 IMPLEMENTATION
PRESENTATION
Prepared by:
DONYES HSAIRI
Notes: Hello again. Thank you for being here today. Last time, we started with first phase of our project. And I already presented the BLE fundamentals…. Since then, I’ve updated the presentation by adding some important details. So today, I’ll mainly explain these new parts and clarify how they complete the overall BLE architecture.

## Slide 2
PLAN
Introduction to Bluetooth Low Energy (BLE).
1
BLE Operations.
3
BLE Architecture and operating principals.
2
Data Access and Security.
4
ESP32-Based BLE Implementation.
5

## Slide 3
What Is BLE ?
Transmit data in short pieces
Small Data Bursts
Wake up briefly for data
Deep Sleep State
Classic Bluetooth uses much power
High Power Consumption
Bluetooth Smart uses less power
Low Power Consumption
Wireless technology for short-range communication.
Developed by the Bluetooth Special Interest Group (Bluetooth SIG).
use much less power and cost less than the Classic.

## Slide 4
Classic Bluetooth vs BLE
Classic Bluetooth
Designed for continuous, high-speed data streaming.
Offers high data rates (1-3 Mbits/s) and strong performance.
High power consumption (~1 W, used as reference).
Transmits data faster , responds to input slower (100 ms wake latency).
BLE (Bluetooth Smart)
Designed specifically for IoT applications.
Sends short bursts of data (ranges across 125 Kbits/s – 2 Mbits/s depending on the mode).
Consumes extremely low power (0.01-0.50W).
Transmits data slower, responds to input faster (6 ms wake latency).
Bluetooth is a wireless technology standard used for exchanging data over short distances.
Notes: We went through

## Slide 6
BLE vs Classic Bluetooth
BLE is the clear winner in terms of energy efficiency.
Keeps devices running for months or even years on a single battery (1–2 years on a 1,000 mAh per cell).
Better choice for low-power, IoT-oriented automotive application, etc.

## Slide 7
BLE Architecture and operating principals
2

## Slide 8
BLE Stack Architecture
The BLE stack implements the core BLE functionality.
It is included as a precompiled library, embedded inside the BLE Component.
The BLE protocol implements a layered architecture:

## Slide 9
The Controller Layer
Controls the hardware that transmits and receives radio waves.
Maps connection requests from the higher layers down to the physical layer.
Responsible for scanning, and for creating and maintaining connections.
Responsible for the actual transmission over the air via radio waves.
Notes: LL is a combination between hardware and software

## Slide 10
Provides a standardized communication interface between the Host Layer and the Controller Layer.
Allows exchanging data and commands.
The HCI
Host Controller Interface.

## Slide 11
The Host Layer
Handles pushing in and pulling out the data of the device.
Defines what data exists on the device.
It is based on Client-Server architecture.
Manages device connections and advertising.
Defines the roles of devices in Bluetooth communication. ( central/ peripheral).
provides a secure connection and exchange between 2 devices.
Provides data encapsulation services.
Ensures data integrity.
Handles packet retransmission, in case it didn’t reach the destination.
Defines a basic data structure.
Defines Data access methods based on the server/client architecture.
Notes: GATT: defines how data can be read or written. GATT server: stores and exposes sensor data (ESP32).
GATT client: initiates commands and requests to the GATT Server

## Slide 12
Host Layer’s Sub-layers Communication
Everything routes through L2CAP: acts as an internal "messaging service" by assigning unique Channel IDentifiers (CIDs) for each sub-layer.
SDUs: Service Data Units PDUs : Protocol Data Units
Notes: Inside the Host, the sub-layers don’t communicate directly and randomly .

## Slide 13
Host Layer’s Sub-layers Communication
L2CAP operations
Segmentation: The process of breaking a single L2CAP SDU up multiple L2CAP packets called SDU segments.
Encapsulation: The process of encapsulating each SDU segment in a proper L2CAP header (PDU length + CID).
Recombination: The process of the controller reassembling fragments into complete L2CAP PDUs.
Fragmentation: The process of breaking down L2CAP PDUs into smaller pieces for the controller to send out.

## Slide 14
Host Layer’s Sub-layers Communication
Data packet format (L2CAP)
Unique ID for the communication channel:
Differentiates the specific connection, ensuring the receiver only listens to packets intended for it.
The core container for the message: Carries the LL header, the application data and security information.
Cyclic Redundancy Check: A mathematical error-detecting code to ensure data integrity.
Alternating sequence of 0s and 1s: Allows receiving radio to wake up, synchronize its timing before the signal data arrives.

## Slide 15
Host Layer’s Sub-layers Communication
Data packet format (L2CAP)
Message Integrity Check: Authenticates the packet to ensure no tampering could happen.
Control information for the LL: How to process the payload and manages the flow of connections.
The actual information: Carries the user application data.
Notes: MIC is optional and only present in encrypted connections

## Slide 16
Host Layer’s Sub-layers Communication
Data packet format (L2CAP)
Logical Link IDentifier: Indicates the type of data contained in the payload (standard application data / LL control command).
Next Expected Sequence Number: Tells the other device which packet SN it expects to receive.
Sequence Number: Identifies the current packet.
More Data: Tells the receiving device that the sender has more packets queued.
Reserved for future Use: Placeholder for future Bluetooth specification updates.
Length: Defines the size of the payload and the MIC combined.
ARQ (Automatic Repeat reQuest) system: Track packets and trigger retransmissions if a packet is lost.

## Slide 17
Host Layer’s Sub-layers Communication
Data packet format (L2CAP)

## Slide 18
Host Layer’s Sub-layers Communication
Data packet format (ATT Protocol PDU)

## Slide 19
The Application Layer
Application logic :
- What data to send. - How to process it.
- How to react to received data.

## Slide 20
Can Developers Control BLE Sub-Layers?
Developers configure the system entirely through APIs exposed to the Application layer by GATT.
Most of the Host's sub-layers (L2CAP, ATT) are not meant to be touched directly. They are handled automatically by the stack.
Notes: Application Programming Interfaces: set of rules or methods that allows one software component to communicate with another without needing to know its internal implementation.

## Slide 21
Can Developers Control BLE Sub-Layers?
What developers can configure through the Application layer's APIs
GAP: device name, advertising data, connection parameters, scanning behavior.
GATT: custom Services and Characteristics (UUIDs, properties, values).
SM: security policy; whether to require bonding, MITM protection, passkey entry, etc.
What developers cannot directly manipulate
The raw ATT protocol frames.
L2CAP packet framing/segmentation.
Internal SMP key-exchange messages.
Notes: These are fixed and standardized inside the Host stack.

## Slide 22
BLE Stack Architecture

## Slide 23
Server-Client Architecture
Receives requests.
Sends back responses.
Initiates requests.
Receives responses.

## Slide 24
Describes how two devices connect and communicate with each other.
Collection of related characteristics that work together to perform a particular function.
Server-Client Architecture

## Slide 25
Define the operations a client can perform on the "Value“.(e.g: read, write,..)
The basic unit of data exchange, encapsulating a specific data value.
(e.g: Temperature value)
Optional parameter attached to a characteristic that provides extra information about it. (e.g: enable/ disable notifications.)
Server-Client Architecture
The actual stored data.

## Slide 26
Services, characteristics, and descriptors are identified by a UUID, so devices know exactly what data they're reading or writing.
Server-Client Architecture

## Slide 27
UUID (Universally Unique IDentifier)
It defines how Bluetooth devices organize and exchange data between devices such as smartphones, gateways, embedded systems, and IoT controllers.
16-bit UUID
provide extended identification space and are less commonly used compared to 16-bit and 128-bit UUIDs.
0x12345678
32-bit UUID
custom UUIDs generally used by manufacturers, industrial systems, and private BLE applications.
550e8400-e29b-41d4-a716-446655440000
128-bit UUID
0x180F
Standardized Bluetooth SIG assigned identifiers commonly used for official BLE services and characteristics.
Description
Example

## Slide 28
Handle
Unique 16-bit address assigned to an attribute within the Generic Attribute Profile (GATT) database (exposed during GATT discovery).
It lets client and server devices directly target specific characteristic values or descriptors without constantly referencing long UUIDs. More efficient, faster, and simpler communication.

## Slide 29
GAP Roles
Central
Initiates connection (scanning).
Processes data.
“Master”
POWERFUL AND RICH RESSOURCES
Peripheral
“Slave”
Advertises its presence.
Accepts connection
LOW-POWER, PROVIDES DATA
Notes: GAP is a set of rules that control how Bluetooth Low Energy (BLE) devices discover, connect, and communicate with each other.

## Slide 30
How to choose master and slave BLE modules ?
Data Role
Device primarily generates data for consumption by other devices (slave) or needs to collect and process data from peripherals (master).
Energy Efficiency
Determine if energy conservation is a top priority for our device.
Slave BLE-module
Connectivity
device needs to connect with multiple other devices.
Master

## Slide 31
GAP Roles
Observer
Connection-less
Smartphone app scans for beacons to detect nearby stores but does not connect to them.
Listens for Bluetooth advertisements but cannot connect to other devices.
Broadcaster
In a mall, phones can receive discount offers but cannot connect to the beacon.
Connection-less
Sends out information but can’t be connected to
Beacon: small, wireless transmitter that uses BLE to broadcast small packets of data.

## Slide 32
Dual-Topology Connections
A device can be simultaneously in a central and a peripheral role.

## Slide 33
Multi-Central / Multi-Peripheral Topology
Multi-Central
A peripheral device can connect to multiple centrals
Multi-Peripheral
A central device can connect to multiple peripherals

## Slide 34
Timing of Parallel Connections
BLE connections use small connection windows to exchange data in every connection interval.
At least an empty packet is sent in every connection interval, first by the central, then by the peripheral.
=> No continuous data receiving is needed.

## Slide 35
BLE Operations
3

## Slide 36
BLE Operations
Read
Write
The core (GATT) operations used to exchange data between a client and a Server.
Notify/Indicate

## Slide 37
Read Operation
On-demand request initiated by the Client to retrieve the current value of a specific data on the Server.
Notes: Client: send a request packet specifying the characteristics. Server: pulls the requested value from its database and replies with a packet containing the data

## Slide 38
Read Operation
Notes: Client: send a request packet specifying the characteristics. Server: pulls the requested value from its database and replies with a packet containing the data

## Slide 39
Write Operation
Initiated by the Client to modify or send data to a characteristic on the Server.
Write Command
Fast throughput.
Lacks data arrival verification.
Write Request
Mechanism
Low throughput due to waiting for acknowledgment.
Cons
Data arrival verified.
Pros
Notes: Throughput is the rate of the useful user data (payload) sent over the air

## Slide 40
Write Request
Write Operation

## Slide 41
Write Command
Write Operation

## Slide 42
Notify Operation
Subscribe to notifications
The Client must "subscribe" to notifications.
Write a specific flag to the characteristic’s Client Characteristic Configuration Descriptor (CCCD).
Push notification packet
The Server pushes a notification packet to the Client whenever the data updates.

## Slide 43
Notify Operation

## Slide 44
Indicate Operation
Notes: The application needs the Client confirmation

## Slide 45
Indicate Operation
Notes: The application needs the Client confirmation

## Slide 46
Data Access and Security.
4

## Slide 47
Data Access
Who can write to a characteristic, and under what conditions?
By default, any connected Client can attempt a write request to the Server.
Whether that write is actually accepted depends on two separate layers of control:
Characteristic Properties
Attribute Permissions
Visibility to client
Primary function
Visible during GATT discovery
Advertised capabilities
Defines conceivable operations
Read, Write, Write Without Response, Notify, etc.
Hidden from the client
The server's real access control.
Enforces access requirements
Encryption, authentication, and authorization requirements.

## Slide 48
Security modes
Pairing Types:
Legacy Pairing: Uses a simple key generation mechanism that doesn't offer the highest level of security.
LE Secure Connections: Uses the Elliptic Curve Diffie Hellman (ECDH) key exchange, providing a higher level of security. This method is particularly effective against passive eavesdropping and MITM attacks.
ECDH: a key agreement algorithm (256-521 bits): Two parties compute the same shared secret without ever transmitting the secret itself.

## Slide 49
Security modes
The Pairing Procedure :

## Slide 50
Security modes
Security mode 1:
This is the standard mode used by the majority of modern BLE applications. It controls link encryption and device identity verification.

## Slide 51
Security modes
Associated Methods:

## Slide 52
Security modes
Security mode 2:
Used when data is not encrypted, but packets must be cryptographically signed to prevent tampering.

## Slide 53
Security modes
Data signing procedure:
Security guard for the integrity and authenticity of data transmitted between devices, even when encryption isn't used.

## Slide 54
ESP32-Based BLE Implementation.
5

## Slide 55
ESP32 Capabilities
Supports GATT Profiles
Handles multiple services and characteristics in one application.
Low cost, low power
Ideal for battery-powered IoT and embedded projects.
Flexible role
Act as a Central, a Peripheral, or even both.
All standard ESP32 microcontrollers feature integrated Bluetooth Classic and BLE.

## Slide 56
BLE Communication Flow Using ESP32

## Slide 57
BLE Communication Flow Using ESP32
Notes: Once the client finds the advertising server, communication can begin.

## Slide 58
Advertising behavior
When and for how long does the server advertise ?
Despite the wide range of advertising interval, most products use the following as a guideline:
Less than 100ms: for very aggressive connections and usually for short periods of time.
100ms to 500ms: normal fast advertising for most devices.
1s to 2s: slow advertising for devices that connect to gateways and where latency is not critical.
Peripheral device enters advertising mode
Notes: Advertising is used either to announce the device’s existence or to transfer data.

## Slide 59
Advertising behavior
Which radio channels are used for advertising ?
BLE uses:
3 primary advertising channels (37, 38 and 39).
37 secondary channels (0 to 36) for active data transfer once the connection is established.
Notes: Once the client finds the advertising server, communication can begin.

## Slide 60
Advertising behavior
When does the peripheral sleep, and when does it wake up?
Before connection
After connection

## Slide 61
Advertising behavior
Does the server keep advertising while already connected?
Stop Advertising
Enter the connected state. Advertising only resumes automatically after a disconnection.
Continue Advertising
If the Peripheral is designed to accept multiple connections, the developer must configure it to keep advertising while already connected.

## Slide 62
Advertising behavior
RSSI (Received Signal Strength Indicator)
The power level (signal strength) of a received Bluetooth packet, measured by the receiving device.
Estimate how close two devices are to each other, although it does not provide an exact distance.
RSSI | Signal Strength | Approximate Situation
-30 dBm | Excellent | Devices are very close (a few centimeters)
-40 dBm | Very strong | Within about 1 meter
-60 dBm | Good | A few meters apart
-80 dBm | Weak | Far away or with obstacles
-90 dBm | Very weak | Near the communication limit

## Slide 63
BLE Communication Flow Using ESP32
Notes: Once the client finds the advertising server, communication can begin.

## Slide 64
Scanning behavior
The peripheral device (broadcaster): sends out advertising packets at regular intervals.
The central device (listener): scans specific (primary) channels to discover the peripheral.
The central relies on :
Scan interval:
Determine how often it checks for advertisement.
Range: 2.5 ms – 10.24 s (0.625 ms unit).
Scan window:
Determine how long it listens during each interval.
Range: 2.5 ms – 10.24 s (0.625 ms unit).
Scan window < Scan interval : For less power consumption.
Scan window = Scan interval : Continuous listening (great for discovery, but rough on battery).
Notes: The scanning phase involves a peripheral device and a central device.

## Slide 65
Scanning behavior
Active scanning
The central receives an advertisement, sends a scan request back to the peripheral.
The peripheral responds with a scan response packet with additional data (longer device name, more service UUIDs, etc).

## Slide 66
Scanning behavior
Passive scanning
The central monitors the advertising channels, logs whatever it receives, and moves on.
This is power-efficient and works perfectly when the advertising packet already contains everything we need to identify the device.

## Slide 67
BLE Communication Flow Using ESP32
Notes: Once the client finds the advertising server, communication can begin.

## Slide 68
Connection behavior
Once the central finds the peripheral, it sends a connection request containing a set of connection parameters that define how the two devices will communicate:
Connection interval: How often they’ll exchange data (7.5ms to 4s, 1.25ms steps).
Peripheral latency: How many communication events the peripheral can skip when idle (0-499)
Supervision timeout: How long without hearing from the peripheral before considering the connection lost (100ms to 32 seconds)

## Slide 69
Connection behavior
How to Pick the Right Connection Interval
Short intervals (7.5-20ms):
High throughput (firmware updates, audio streaming).
Latency matters (medical devices with real-time feedback).
The devices are plugged in or battery life isn’t the primary constraint.
Medium intervals (20-100ms):
Moderate throughput (fitness data during a workout).
Occasional responsiveness is important but not real-time.
Balancing battery life with user experience.
Long intervals (100ms+):
Sending infrequent data (temperature readings every few seconds).
Battery life is the primary constraint.

## Slide 70
Connection behavior
If the interval is too short:
Battery drains faster than expected.
The OS might override some parameters to protect battery life.
How to Pick the Right Connection Interval for Your Use Case
If the interval is too long:
Users perceive lag when interacting with the device.
Throughput is lower than needed (firmware updates take forever).
Notifications and indications feel sluggish.

## Slide 71
Connection behavior
Peripheral latency
If the peripheral latency is too aggressive:
Central can’t get responsive communication when it needed, making actions initiated by the central seem slow.
It lets the peripheral skip connection events when it has nothing to send, without the central assuming the connection is dead.
=> The central keeps the connection alive, but the peripheral is burning almost no power during these gaps.

## Slide 72
Connection behavior
Detect dead connections
Supervision timeout
If the supervision timeout is too long:
When devices disconnect, it takes forever to detect and clean up.
If the supervision timeout is too short:
False disconnections.
More reconnection attempts, more power consumption.
Supervision timeout > (1 + Peripheral latency) × Connection interval × 2

## Slide 73
BLE Communication Flow Using ESP32
Notes: Once connected, both devices will be ready for data exchange. GAP: - Manages device connections and advertising.
-Defines the roles of devices in Bluetooth communication. ( central/ peripheral).

## Slide 74
BLE Communication Flow Using ESP32
Connection establishment
Notes: When communication is no longer needed

## Slide 75
BLE Communication Flow Using ESP32
Notes: GAP: - Manages device connections and advertising.
-Defines the roles of devices in Bluetooth communication. ( central/ peripheral).

## Slide 76
BLE Communication Flow Using ESP32
GATT discovery
Each attribute consumes handles (with a limit of 40 handles):
Service: 1 handle.
Characteristic: 2 handles (declaration, value).
Descriptor: 1 handle.
Notes: Once connected,

## Slide 77
BLE Communication Flow Using ESP32
Notes: Once connected, both devices will be ready for data exchange.

## Slide 78
BLE Communication Flow Using ESP32
Notes: When communication is no longer needed

## Slide 79
BLE Communication Flow Using ESP32

## Slide 80
Testing Tools
Build / Test (PC)
BLE Server
ESP32
BLE Client
brave://bluetooth-internals/#devices
Bluetooth LE explorer
Server (esp32), Client (PC)

## Slide 81
Testing Tools
Build / Test (Phone)
BLE Client
nRF Connect
LightBlue
BLE Server
ESP32
Server (PC), Client (esp32)

## Slide 82
Testing Tools
Build / Test (PC)
BLE Client
ESP32
Server (esp32), Client (PC)
BLE Server
Vscode

## Slide 83
Thank You !
Prepared by:
DONYES HSAIRI